## Slide 1: FortiGate Site-to-Site VPN Lab in FortiOS 7.4

## Slide 2: Objective of the Lab
Configure a secure Site-to-Site VPN between two Fortigate firewalls to enable encrypted communication between two remote networks.

## Slide 3: Topology
Network A (HQ) Network B (Branch)
[FortiGate-1] ----Internet---- [FortiGate-2]
192.168.1.0/24 192.168.2.0/24

## Slide 4: Components Used
2x FortiGate Firewalls (Minimum FortiOS 7.4)
Network switches
Computers for testing
Internet connection

## Slide 5: Network Configuration Details
FortiGate-1 WAN IP: 203.0.113.1
FortiGate-1 LAN: 192.168.1.0/24
FortiGate-2 WAN IP: 203.0.113.2
FortiGate-2 LAN: 192.168.2.0/24

## Slide 6: VPN Configuration Steps
Step 1: Interface Configuration
1. Configure WAN interfaces
2. Configure LAN interfaces
3. Ensure routing between interfaces

## Slide 7
Step 2: IPsec VPN Configuration
1. Create Phase 1 (ISAKMP) proposal
Authentication method: Pre-shared key
Encryption: AES-256
Hash: SHA-256
Diffie-Hellman Group: 14
2. Create Phase 2 (IPsec) proposal
Encryption: AES-256
Hash: SHA-256
PFS (Perfect Forward Secrecy): Enable

## Slide 8
Step 3: Tunnel Interface Setup
Create tunnel interfaces on both FortiGates
Assign IP addresses to tunnel interfaces
Configure static routes via tunnel Step 4: Firewall Policies
Create inbound and outbound policies
Allow necessary traffic between networks
Apply security profiles

## Slide 9: Testing the Lab
1. Ping tests between networks
2. Traceroute verification
3. Bandwidth and latency measurements
4. Check VPN tunnel status

## Slide 10: Expected Results
- Stable VPN connection
- Encrypted traffic between networks
- Minimal latency
- No packet loss

## Slide 11: Potential Troubleshooting
- Verify Phase 1 and Phase 2 settings match
- Check firewall policies
- Validate routing configurations
- Monitor system logs

## Slide 12: Security Recommendations
Use strong pre-shared keys
Implement regular key rotations
Enable logging and monitoring
Keep FortiOS updated